## Slide 1
      Team Name: SixG_ISAC
Team Github Repo: ITU-AI-ML-in-5G-Challenge/ML5G-PS-004-Depth-map-estimation-in-6G-mmWave-systems
        Team Members:
          Shubham Khunteta
          Yeswanth Reddy Guddeti
          Avani Agrawal
          Ashok Kumar Reddy Chavva
        Affiliation : Beyond 5G Team, Samsung R&D Institute India, Bengaluru.
        Problem Organizer: NIST, USA.
ITU AI/ML in 5G challenge: ITU-ML5G-PS-004
Presentation Title : Depth Map Estimation in 6G mmWave systems
Notes: Hello everyone, (hope you enjoyed the presentations so far). I am Yeswanth reddy from Samsung research institute in Bangalore. Our team SixG_ISAC has four members, myself, shubham, avani and ashok .
And we work on applications that go beyond 5G.
To support a large variety of such applications we need a network that is not just fast but also flexible with intelligence to adapt to each of these applications .
In this challenge, Our goal is to develop a machine learning framework for one of these applications i.e estimation of depth map of the environment using 6G communication signals.

## Slide 2
Motivation : Communication waves to create Digital world
Physical world
Digital world
ISAC + AI/ML
Integrated Sensing & communications
Inference using RF communication signal
  Reuse spectrum, devices and protocols to perform both communication and sensing.
  Extra processing required to acquire multi-dimensional data
Notes: Integrated sensing & communications or ISAC in short uses existing Communication infrastructure like spectrum, devices and protocols to perform both communication and sensing.
There has been lot of literature in this area where inferences were made on signal distortions to detect location ,movement & even orientation of people & obstacles.
-----Transition------
The next step envisioned in this direction is creating digital twin of the physical world . This digital twin can then be used to solve problems like beam selection virtually without ever sending actual beams in physical environment.
On the other hand, Creating a digital twin using RF signals implies sensing a whole room having hundreds of objects . Therefore We can no longer rely only on the handcrafted features for inferences as this problem is of higher complexity & scale.
We also need to perform extra processing to obtain multi dimensional data from RF signals.
(How MIMO vs LIDAR different ??? ADD pros vs CONS : low light,NLOS)
Traditionally this depth map has been done using LIDAR & camera. So we need to train a model with large enough training set with RF signals as input and lidar or camera data as ground truth.
Thanks to measurement setup from NIST which has RF, lidar sensors mounted on a Robot , we have been provided with data from multiple locations across a conference room.
Now moving onto the solution, I will be handling the first half of the presentation explaining the problem statement and the pre-processing of the RF data before it goes into the ML model. Shubham will then explain the ML model architecture, training and the results.

## Slide 3
Problem statement
Problem statement
Challenge : Estimate the depth map of the environment at each receiver position, using mm-wave signals + ML.
RX
TX
  One fixed transmitter
  One moving receiver
ML Model :
Trained Model
Input Data:
Training RF Dataset
Output: LiDAR Point Clouds
Channel Impulse response
Setup :
  TX/RX
  Location & Orientation Unknown
Notes: Lets take a look at the measurement setup. This is the room in which measurements are taken. (laser pointer)
We have a transmitter at a fixed location on the left and a receiver moving in different areas of room . Observation of the room changes with receiver location & orientation -----Transition------
The challenge is to estimate depth map of the environment at each receiver position using mmwave signals.
-----Transition------
In other words , We train an ML model that takes MIMO channel impulse response as input and generates Lidar point cloud as the output.
-----Transition------
Note that We are only given channel impulse response as input. The location & orientation of these nodes are therefore unknown making the problem more complicated.

## Slide 4
Solution outline
Solution : At each RX location
Transform bi-static RF data to mono-static format.
Train ML model by fitting it to similarly structured LiDAR ground truth.
RX
TX
TX/RX
RX
Ground Truth:
Training LiDAR dataset
ML Model
Input Data:
Training RF Dataset
Pre-processing
Notes: Now coming to outline of solution.
The input RF data has the transmission & reception at physically seperate locations also known as bi static mode. Whereas Lidar sends and receives laser signals from the same location also known as mono-static mode.
-----Transition------
So Pre-processing step handles the deterministic aspects of transforming MIMO channel data which is in bistatic format to mono-static format. This makes ML model learning faster & understandable.
-----Transition------
Looking at the input data at each location, we observed
that RF data has lower resolution & fewer reflections (with 6400 points) whereas Lidar has both higher resolution & larger points of reflections (approximately 32,000 points).
-----Transition------
So at each RX location,
We transform the bistatic RF data into mono-static format
And train the ML model by fitting it to similarly structured Lidar ground truth.
--------end--------------
As you can see,
In essence, we are attempting to take MIMO channel data that is bi-static (physically separable TX, RX) and fit it to LIDAR data that is mono static (same antenna as TX & RX).
(Why do you need to transform to mono static data before sending to ML?
We wanted to make the training part of model more simpler & explainable . If not done, model should be itself learn about existence of MIMO TX and its location and other features thorough a large amount of training data which is of-course not guaranteed and depends on ML architecture.)
(In addition, we wanted to handle the deterministic aspects of model fitting like data transformations outside the DL model training.
Since we are aware of what part of model learns what? this makes improving the overall model with further additional features much easier.)

## Slide 5
Pre-processing : Spatial Transform
TX Ant x RX Ant x time
(TX Ant x RX Ant x Delay)
Spatial transform
(AOD x AOA x Delay)
Channel Impulse response
Transforms Communication data to Sensing framework
Delay Distance resolution of .
Horz.Ant 8 Azimuth resolution of 22.5 o (Avg.)
Vert.Ant 8 Elevation resolution of 22.5 o (Avg.)
8×8
8×8
Notes: First step in pre-processing to perform spatial transform on the input channel impulse response. This is done so that we can transform our data from Antenna space to angular beam space.
-----Transition------
This spatial transform therefore helps us get to sensing framework from communication framework.
-----Transition------
((laser pointer) On the right , you have a plot of matrix H_beam for a delay where each entry represents power for an AOA,AOD pair)
The matrix H_beam gives us the power of reflections at points separated in distance by 0.17 m or 17 cm & on avg. in angle by 22.5 deg across azimuth & elevation

## Slide 6
Pre-processing : Spatial Transform
TX
Spatial transform
(AOD x AOA x Delay)
Notes: Now that we got H_beam, we need to transform it into mono-static format (i.e as if the transmission & reception occur at RX.)
The first step in this transformation is to Find LOS path

## Slide 7
Pre-processing : Find LOS
TX
Spatial transform
1 : Find LOS
Select (TX,RX) Beam with
Higher Power
Lower Delay
Tighter Beamwidth
Remove LOS from & Store LOS parameters
(AOD x AOA x Delay)
Notes: (laser pointer) To find LOS , We select the beam which has higher power, lower delay, tighter beamwidth.
------- Transition------
Since the LOS doesn’t have info about environment we remove those entries from H_beam.
But we store the LOS path parameters as they give location & orientation info of RX which will be used in subsequent steps

## Slide 8
Pre-processing : Remove TX
TX
Spatial transform
1 : Find LOS
(AOD x AOA x Delay)
2 : Remove TX
(AOA x Delay)
Remove effect of TX by projecting AOD to Delay
Notes: Next, we remove the effect of TX in the matric H_beam to get power map from RX perspective .
---Transition ---
We do this by projecting AOD dimension to delay dimension

## Slide 9
Pre-processing : Remove TX
TX
Spatial transform
1 : Find LOS
AOA
AOD
Delay
2 : Remove TX
(
AOA
Delay
(AOA x Delay)
Project AOD to Delay
RX
Calculate
TX
RX
Notes: (laser pointer) The signal shown here departs TX travels r2 distance hitting an obstacle and then travels r1 distance before arriving at RX . It travels r1+r2 distance from TX. so we need to shift the delay of this entry in H_beam from r1+r2 to r1 so that it appears to arrive at RX directly from reflection point.
SO we need to calculate ratio r2/r1.
----Transition----
(laser pointer) In this triangle made from LOS path and the Current reflection , the angle delta AOD is difference between Angle of departure of LOS and of the current reflection . Delta AOA can be defined similarly. Here we use LOS parameters saved in the previous step.
Applying sine theorem we can obtain the ratio r2/r1 as ratio between sines of delta AOA to delta AOD
Now we can project entries in AOD dimension to appropriate delay to get power map from RX perspective.

## Slide 10
Pre-processing : Remove TX
TX
Spatial transform
1 : Find LOS
(AOD x AOA x Delay)
2 : Remove TX
(AOA x Delay)
Remove effect of TX by projecting AOD to Delay
Notes: Therefore we remove the effect of TX by projecting AOD dimension to delay dimension

## Slide 11
Pre-processing : Rescale Power
Spatial transform
1 : Find LOS
2 : Remove TX
3 : Rescale power
TX
(AOA x Delay)
(AOA x Delay)
Rescale to get monostatic power
(AOD x AOA x Delay)
(AOA x Delay)
Notes: The last step remaining is to scale the power so that the reflections appear to travel the Receive path twice.

## Slide 12
Pre-processing :
Spatial transform
1 : Find LOS
2 : Remove TX
3 : Rescale power
TX
Y (m)
Z (m)
X (m)
Input: CIR for 64x64 MIMO
Notes: With this, we have finished pre-processing where we have taken channel impulse response in bi-static format as input and obtained RX power which is in mono-static format similar to lidar as output
Now it’s ready to be sent to the ML model.
--Transition---
The plot shows pre-processed data for a single RX location. We see power at RX. across 64 different AOAs and 100 delays in each direction
Shubam will now explain the ML model and results of training.

## Slide 13
Y (m)
Z (m)
X (m)
Input and Output for ML Model Training
Given Input: CIR for 64x64 MIMO
Input for the ML model:
Power of reflections from :
64 directions : (8 Az x 8 El)
Each direction 100 points*.
Pre-processing
Given Output (ground truth): LIDAR PCD
*Distance between consecutive points ~ 17cm
Output labels for ML model: Voxel Grid:
Voxel size =0.25 m -> Dim: 128 x 128 x 16
Voxel size=0.5 m -> Dim: 64x64x8
If a point is in voxel: Voxel value =1
ML Model
~ 35k points
[1.233, 8.342, -1.20]
[4.25, 10.57, -0.25] ….
RX
TX
(-16, -16, -2)
(16, 16, 2)
(-16, -16, -2)
(-16, -16, -2)
(16, 16, 2)
(16, 16, 2)
~ 13k voxels are 1 out of : 128 x 128 x 16 voxels
(-16, -16, -2)
(16, 16, 2)
Voxel Grid
Notes: Input:
So far, We pre-processed the input CIR data and obtained the power of reflections at receiver from 64 directions and 100 points in each direction. This is the input for the ML model.
# This translate to 17m of radius as the range resolution is 17cm.
----------
#Output:
- Now, I will explain the output for the ML model
Given output for the challenge is LIDAR PCD of the room as seen by the receiver
#one LIDAR PCD contains ~35k points which are coordinates of obstacles and it looks like this figure
For the ML model training, Input and output data is given for multiple locations across the room.
Perception of the room as seen by Rx changes with the change in Rx location and orientations. And here are some snapshots of output data across locations explaining this behaviour.
Assuming Rx is at origin, we observed, across the locations, LIDAR points are inside of the bounding box with min_bound = [-16, -16,-2] and max_bound=[16,16,2]
So, we use a voxel grid as the output for the ML model with these min and max bounds.
With voxel size =0.25 m, the dimension of voxel grid 128x128x16, if we use voxel-size as 0.5m, the voxel grid size reduces by 8.
#Note that, 35k points of lidar PCD, fits into 13k voxels of voxel grid of voxel-size 0.25m
Higher the voxel size, complexity of the ML model will be lower, but resolution of the output will also be lower , so there is a trade-off !

## Slide 14
Solution : Why is it difficult ?
Y (m)
Z (m)
X (m)
Lidar
RF
ML Model
 | Pre-processed RF data | LIDAR Data
Range resolution | 0.17 m | 10^-6 m
Angle resolution | Low (~ 22.5 o ) | High
I/O Dimension | 6400x1 | 2,62,000 voxels (voxel grid: 128x128x16)
Location of the Tx and Rx is unknown |  | 
Solution is novel and first of its kind.
Notes: - Why this problem is so challenging to solve ?
- There have been enough research on camera image as input to depth map estimation and few works on high resolution LIDAR as input and Radio signals as output.
- Here, We have the RF data as input which has way less resolution than the output LIDAR data in terms of range and angle.
because lidar is at higher freq and guided by laser beam, while RF sensing limited by sampling rate and no. of antennas.
Lidar gives more reflections compared to RF sensor.
Here, Input dimension is quite lower than the output dimension (I/o = 3% )
Apart from this, for this challenge, Tx and Rx locations are also unknown.
#Range resolution of the RF data is 0.17 m while that of lidar data is 10^-6 m observed
#Angle resolution of the RF data is also poor (around 22.5 deg) compared to high resolution lidar.

## Slide 15
ML model architecture
Motivation behind used layers:
Up-sampling layer
  Ratio I/O dimension=3%
CNN layers:
  Correlation in reflections exists in close neighbourhood
Y (m)
Z (m)
X (m)
From Pre-processing step:
Notes: Now, I will explain the ML model
The pre-processed CIR, which is mono-static Rx power is fed to dense layer, followed by Upsampling layer and CNN layers to predict the voxel grid and further, the Point cloud data.
we use upsampling layer becasue I/O dimension ratio is less, ~3% as the input dimension is 6400 and output dimension is 128x128x16,
we use CNN layers because Correlation in the reflections exists in the neighbourhood,

## Slide 16
Custom Loss function: binary cross entropy with weights where and .
  As the output voxel grid is sparse, training is skewed towards the label ‘1’.
Training parameters
Dataset:
Total training samples : 3400 samples
  Area 1 : 2400 samples
  Area 3: 1000 samples
Validation samples : 350 (consisting of both the areas)
Test data: 529 samples of Area 2
Optimizer:
  Adam with learning rate of 0.0005
  Decay rate: 0.9 every 10000 steps
Epochs =100, batch size : 32.
RX
TX
Training samples
Testing samples
~ 13k voxels are 1 out of : 128 x 128 x 16 voxels
Notes: -Coming to training parameters:
We use Custom loss function which is similar to binary cross entropy loss function with added weights for the labels. Higher weight is given to 1 since in the output voxel grid of size 128x128x16, only 13k voxels are 1.
We train the model with 3400 samples captured across various location as shown in the figure.
Testing data consist of CIR for 529 locations.
We train this model with adam optimizer with decaying learning rate of 0.0005.
(2min+30sx3=1.5min=3.5min)

## Slide 17
LIDAR PCD (Ground truth) | Predicted PCD
Prediction vs Actual LIDAR PCD
LIDAR PCD (Ground truth) | Predicted PCD
The ML model proposed returns LIDAR-like high resolution point clouds
Change in perception, is nicely captured even though the Tx and Rx locations are unknown.
(-16, -16, -2)
(16, 16, 2)
(-16, -16, -2)
(16, 16, 2)
(-16, -16, -2)
(16, 16, 2)
(-16, -16, -2)
(16, 16, 2)
Notes: Here are some snapshots of the Actual LIDAR PCD and predicted PCD, we can see that the
The ML model proposed returns LIDAR-like high resolution point clouds
Change in perception across location and orienatation, is nicely captured in the predicted PCD even though the Tx and Rx location is unknown for the challenge.

## Slide 18
Evaluation Metric for the challenge
Output: Predicted PCD
Ground Truth: LiDAR Evaluation dataset
Evaluation
Trained Model
Input Data: RF Data Evaluation Dataset
Chamfer Distance
measures discrepancies between point clouds.
Predicted PCD:
LIDAR PCD:
Notes: - As we have seen the quality of the prediction given the difficulty of the challenge, Now we explain the quantitative evaluation metric of the challenge :
- So, here Chamfer distance is used for evaluation: chamfer distance measures the discrepancies between the point clouds and return how close the two point cloud are. Lower the chamfer distance, closer or similar they are.

## Slide 19
Evaluation : Error Analysis on Testing Data
Chamfer distance for Training data
Average Chamfer distance = for voxel-size=0.25 m
Average Chamfer distance = 2.2 for voxel-size=0.5 m
Chamfer distance for Testing data
Average Chamfer distance = which is good for the room of size ̴16 m x 16 m x 4 m
Average Chamfer distance = 1 for the samples which are closer to the Tx.
RX
TX
Testing samples
Test data: 529 locations
Chamfer distance
Chamfer distance
Test data: 529 locations
Chamfer distance
Notes: - Now, I will explain the error analysis done in terms of chamfer distance.
We have plotted the chamfer distance for the testing data which is collected along the purple colored route in the room. Transmitter location is at the bottom left corner.
Here blue means chamfer distance of 1m^2 and red means 9m^2, We see that most the samples are blue which suggest the prediction is good for the room dimension of 16x16x4.
We also observe from the figure that the average chamfer distance across the locations for testing data is ~2m^2,
While for the samples which are closer to Tx, Chamfer distance is ~ 1m^2.
We also did the error analysis on training data along the blue route for different voxel- sizs. We found that voxel-size 0.25m provide better chamfer distance ~ 1.5m^2 compared to the 2.2m^2 for voxel-size 0.5m, and that is why we use the voxel-size0.25m in the proposed algorithm.
--The problems and the proposed algorithm are the first of its kind and as far as we know there is no baseline for this solution to compare with.
3.5min +30sec*3=5min

## Slide 20
Conclusion and Future work..
Thank you.
Questions ?
We thank the NIST, USA and ITU challenge team for providing this exciting problem.
Observations:
The ML model proposed returns LIDAR-like high resolution point clouds.
Change in perception of room across locations, is nicely captured in the predictions.
Average Chamfer distance = which is good for the room of size ̴16 m x 16 m x 4 m
Average Chamfer distance = 1 for the samples which are closer to the Tx.
Future Work :
Train the network with higher resolution input data.
Experiment with the Voxel grid size
Global training inclusive of all the locations
Train using Tx perspective along with Rx perspective
Notes: - At last, we summarize the observations :
1
2
3 &4
The future work includes training with higher resolution inputs
and high resolution output in the Ml model with lowering voxel size.
- We will also experiment with including all the locations for prediction of the depth map
Thank you for listening, any questions ?
5 min 30sec.